## Slide 1: Source Routing for Downward Data Traffic
WSN Lab final project, 2017-2018

## Slide 2: Upward traffic
Root
Many-to-one, up the tree
Notes: Each node sending its data to its parent which then forwards to its parent until it reaches the destination. The control messages were coming from the root and data from the source

## Slide 3: Source Routing – overview
Source specifies the entire packet route: complete path from source to destination
Computed by the root node only
Intermediate nodes just forward to specific next hop:
#2 would look at path in header and forward to #4, and so on until the packet reaches the destination node D = 8

## Slide 4: Downwards Source Routing – overview
Root
Enable the sink to send data down the tree
Notes: Each node sending its data to its parent which then forwards to its parent until it reaches the destination. The control messages were coming from the root and data from the source

## Slide 5: To begin with:
Objective: Node S wants to send data to node D
Doesn’t know the route to D
R1
S
R3
R2
D
R4
R5
Root
Notes: In source routing, the node that wants to send the data requests for the path to that node. For eg, we want to send the data from S to D, where S is the root in this case.

## Slide 6: Phase 1: Collecting the routing information
R1
S
R3
R2
D
R4
R5
D’s parent is R3
Child | Parent
D | R3
Send using the
Data collection protocol
Notes: So phase 1 is route discovery. In this phase, you will used the data collection protocol that you have already implemented to send the route info back to S. This route info is like a control traffic from node D to S which will be used by node S in order to reach D. Once this info is sent to S, it will create a table storing the child and the parents (path to reach each node in the network).

## Slide 7: Phase 1: Collecting the routing information
R1
S
R3
R2
D
R4
R5
R3’s parent is R2
Child | Parent
R3 | R2
D | R3
Notes: So phase 1 is route discovery. In this phase, you will used the data collection protocol that you have already implemented to send the route info back to S. This route info is like a control traffic from node D to S which will be used by node S in order to reach D. Once this info is sent to S, it will create a table storing the child and the parents (path to reach each node in the network).

## Slide 8: Phase 1: Collecting the routing information
R1
S
R3
R2
D
R4
R5
R2’s parent is R1
Child | Parent
R2 | R1
R3 | R2
D | R3
Notes: So phase 1 is route discovery. In this phase, you will used the data collection protocol that you have already implemented to send the route info back to S. This route info is like a control traffic from node D to S which will be used by node S in order to reach D. Once this info is sent to S, it will create a table storing the child and the parents (path to reach each node in the network).

## Slide 9: Phase 1: Collecting the routing information
R1
S
R3
R2
D
R4
R5
R1’s parent is S
Child | Parent
R1 | S
R2 | R1
R3 | R2
D | R3
Notes: So phase 1 is route discovery. In this phase, you will used the data collection protocol that you have already implemented to send the route info back to S. This route info is like a control traffic from node D to S which will be used by node S in order to reach D. Once this info is sent to S, it will create a table storing the child and the parents (path to reach each node in the network).

## Slide 10: Phase 1: Collecting the routing information
R1
S
R3
R2
D
R4
R5
Child | Parent
R1 | S
R2 | R1
R3 | R2
D | R3
R5 | R4
R4 | R2
Source routing table
(at the root only)
Notes: Now we have the full source routing table stored at the root

## Slide 11: Topology Reports
Dedicated Topology Reports:
  Dedicated control traffic to inform the sink of the parent of each node
Piggybacking: attach topology reports to data collection packets
  When the application sends a packet, e.g., using: my_collect_send()
  Include a header with the parent of the sender
Child | Parent
R1 | S
R2 | R1
R3 | R2
D | R3
R5 | R4
R4 | R2

## Slide 12: When Sending Packets
When node S sends a data packet to D, it checks a source routing table. If route exists, then entire route is included in the packet header
  Hence the name source routing
Algorithm:
  Assign N:=D
  Search for node N in the table to find N’s parent P
  If N is not found or a loop is detected, drop the packet
  If P ==root, transmit the packet to next-hop node N
  Else add N to the source routing list of the packet, assign N:=P,
  go to step 2
Child | Parent
R1 | S
R2 | R1
R3 | R2
D | R3
R5 | R4
R4 | R2

## Slide 13: Source Routing - Phase 2: Data Delivery
Objective met
R1
S
R3
R2
D
R4
R5
Child | Parent
R1 | S
R2 | R1
R3 | R2
D | R3
R3,D
Payload
Payload
R2,R3,D
Payload
R1,R2,R3,D
Payload
Only sink can initiate downward traffic
Notes: Once the source routing table is constructed, S can now use it to reach the specific node. In this case to reach node D.
Now many nodes can reach to root (many to one) and the root can reach to other nodes (one to many) creating a bidirectional data communication mechanism.

## Slide 14: Source Routing – Loop detection
R1
S
R4
R1
S
R4
Child | Parent
R1 | R4
R4 | R1
If the message “R4’s parent is S”
is lost, we have a loop:
Child | Parent
R1 | S
R4 | R1
Child | Parent
R1 | R4
R4 | S
Intended record
Stale record
Notes: So phase 1 is route discovery. In this phase, you will used the data collection protocol that you have already implemented to send the route info back to S. This route info is like a route reply from node D to S which will be used by node S in order to reach D. Once this info is sent to S, it will create a table storing the child and the parents (path to reach each node in the network).

## Slide 15: Program Structure
Your program should enable:
  Many-to-one data collection (you already have)
  One-to-many data delivery from the sink to whichever network node
  The one-to-many interface should provide two main functions:
    Send Function: int sr_send(struct my_collect_conn *c, const linkaddr_t *dest);
    Recv Callback: void sr_recv(struct my_collect_conn *c, uint8_t hops);
  The top-level application should use these functions